## Slide 1: Non-traditional Machining Processes
Prepared By
Prof A. L. Suradkar

## Slide 2: Non-traditional Machining Processes
Manufacturing processes can be broadly divided into two groups:
primary manufacturing processes : Provide basic shape and size
secondary manufacturing processes : Provide final shape and size with tighter control on dimension, surface characteristics
Material removal processes once again can be divided into two groups
Conventional Machining Processes
Non-Traditional Manufacturing Processes or non-conventional Manufacturing processes
Conventional Machining Processes mostly remove material in the form of chips by applying forces on the work material with a wedge shaped cutting tool that is harder than the work material under machining condition.

## Slide 3: Non-traditional Machining Processes
The major characteristics of conventional machining are:
  • Generally macroscopic chip formation by shear deformation
  • Material removal takes place due to application of cutting forces – energy domain can be classified as mechanical
  • Cutting tool is harder than work piece at room temperature as well as under machining conditions
Non-conventional manufacturing processes is defined as a group of processes that remove excess material by various techniques involving mechanical, thermal, electrical or chemical energy or combinations of these energies but do not use a sharp cutting tools as it needs to be used for traditional manufacturing processes.
The major characteristics of Non-conventional machining are:
1. Material removal may occur with chip formation or even no chip formation may take place. For example in AJM, chips are of microscopic size and in case of Electrochemical machining material removal occurs due to electrochemical dissolution at atomic level.

## Slide 4: Non-traditional Machining Processes
The major characteristics of Non-conventional machining:
2. In NTM, there may not be a physical tool present. For example in laser jet machining, machining is carried out by laser beam. However in Electrochemical Machining there is a physical tool that is very much required for machining
3. In NTM, the tool need not be harder than the work piece material. For example, in EDM, copper is used as the tool material to machine hardened steels.
4. Mostly NTM processes do not necessarily use mechanical energy to provide material removal. They use different energy domains to provide machining. For example, in USM, AJM, WJM mechanical energy is used to machine material, whereas in ECM electrochemical dissolution constitutes material removal.

## Slide 5: Needs for Non Traditional Machining
Extremely hard and brittle materials or Difficult to machine materials are difficult to machine by traditional machining processes.
When the work piece is too flexible or slender to support the cutting or grinding forces.
When the shape of the part is too complex.
Intricate shaped blind hole – e.g. square hole of 15 mmx15 mm with a depth of 30 mm
Deep hole with small hole diameter – e.g. φ 1.5 mm hole with l/d = 20
Machining of composites.

## Slide 6: Classification of Nontraditional Processes by Type of Energy Used
Mechanical ‑ erosion of work material by a high velocity stream of abrasives or fluid (or both) is the typical form of mechanical action
Electrical ‑ electrochemical energy to remove material (reverse of electroplating)
Thermal – thermal energy usually applied to small portion of work surface, causing that portion to be removed by fusion and/or vaporization
Chemical – chemical etchants selectively remove material from portions of workpart, while other portions are protected by a mask

## Slide 7: I. Mechanical Energy Processes
Ultrasonic machining
Water jet cutting
Abrasive water jet cutting
Abrasive jet machining

## Slide 8: II. Electrochemical Machining Processes
Electrical energy used in combination with chemical reactions to remove material
Reverse of electroplating
Work material must be a conductor
Processes:
  Electrochemical machining (ECM)
  Electrochemical deburring (ECD)
  Electrochemical grinding (ECG)

## Slide 9: Thermal Energy Processes
Electric discharge machining
Electric discharge wire cutting
Electron beam machining
Laser beam machining
Plasma arc machining

## Slide 10: IV. Chemical Machining (CHM)
Material removal through contact with a strong chemical etchant
Processes include:
  Chemical milling
  Chemical blanking
  Chemical engraving
  Photochemical machining
All utilize the same mechanism of material removal

## Slide 11: Grinding

## Slide 12: Abrasive Grinding
Can be viewed as multiple very small cutting edges
Results in a very fine finish
Can leave residual stresses
Slow, small material removal rates
Sparking out

## Slide 13: Standard Grinding Wheel Designation
While this is specific to grinding, realize that there are similar standard designations in most industries
Take the time to learn the standard designations early so that you can speak intelligibly with those within the industry.

## Slide 14
Cold Working
1. Plastic deformation which is carried out in a temperature region and over a time interval such that the strain hardening is not relieved is called cold working.
2. Cold working produces additional dislocations within the metal structure
3. Initially the dislocations can move through the metal structure.
4. As the working continues, however, the movement of the dislocations becomes more difficult.
5. The metal becomes less malleable and ductile.
What Does Cold Working Effect?
The following properties are affected by cold work significantly:
1. Tensile Strength
2. Hardness
3. Yield Strength
4. Ductility